## Slide 1
Design of a Two-Tier QoS-Aware Scheduler for Private 5G
A convex rate planner on a ~1 s horizon, over a per-slot drift-plus-penalty tracker.
Motivation, design, and simulation results against the scheduler OpenAirInterface ships — with what remains to land it on hardware.

## Slide 2
MOTIVATION
The factory floor asks for three different things
One private 5G cell, one carrier, and traffic classes that differ in kind rather than in volume:
Class | Example | What it needs | How you know it failed
GBR | Robot camera and LIDAR uplink | A sustained rate floor | Dropped frames, blind robot
Delay | Motion control, teleoperation | Bytes before a deadline | A late command — a safety event
Best-effort | Firmware push, log upload | Whatever is left | Slower; nobody notices
OpenAirInterface's NR MAC schedules with a proportional-fair metric over per-UE grants. PF has no term for a rate contract, no term for a deadline, and no configured-grant path for periodic traffic. It is a good answer to a question the factory is not asking.
A robot whose video is switched off entirely is a failure in a way a uniformly degraded fleet is not — a distinction a throughput-fair metric cannot see, let alone act on.

## Slide 3
INFORMING THE DESIGN
What the prior art told us to do — and not to
Adopted
Two timescales. A slow declarative program over a fast per-slot controller — the pattern behind NVS (Kokku 2012) and the O-RAN RIC split. We instantiate it; we do not claim it.
Network utility maximisation (Kelly 1998) for the slow tier — an objective a plant engineer can read and audit.
Drift-plus-penalty (Neely 2010) for the fast tier — it solves the per-slot problem, and needs a target, which Tier-1 supplies.
Configured grants dominate latency for time-critical industrial traffic (Larrañaga 2023, ns-3 / 5G-LENA).
Ruled out, and why
Tuned PF variants — M-LWDF, Exp-rule. Excellent on delay; on rate they saturate, because a multiplicative deficit weight equalises a weighted 1/R_avg and cannot reach an arbitrary unequal target. Monghal (2008) measured exactly that.
Learned schedulers. Kela (2024), arguing from inside that literature, finds deployable deep schedulers do not yet exist — real-time cost, 3GPP compliance, and poor generalisation across bandwidth and traffic mix.
Two commitments follow: an integrator, not a metric multiplier in the fast tier, so an arbitrary target vector is reachable; and a convex program with one auditable fairness dial in the slow tier.

## Slide 4
THE DESIGN · EVERY ~1 S
Tier-1: what rate should each flow target?
Rates r_i ≥ 0, slacks s ≥ 0, one feasible set F(floor):
Σ_{i∈d} r_i / SE_i ≤ C_d
capacity in PRB-symbols, special slot included
r_i + s_i ≥ G_i
GBR contract — soft, so overload stays feasible
r_i ≥ floor_i
max-min floor — hard
Σ_{i∈σ} r_i/SE_i + s_σ ≥ φ_σ·C_d
slice share — soft, demand-capped, work-conserving
Solved in three stages, in that order:
A. t* = max t s.t. r_i ≥ t·Ĝ_i ∀ GBR
then floor_i = α·t*·Ĝ_i
B1. S* = min Σ p_i·s_i + p_σ Σ SE_σ·s_σ
B2. max Σ w_c·log(r_i+ε) s.t. Σ p_i·s_i ≤ S*
Order the objectives; do not weight them. Folded into one, the two terms sit 3.3×10⁷ apart — two solvers returned optimal_inaccurate and disagreed 3.6× on one flow's rate. Split into B1 then B2, both match the analytic optimum to 100 bps.
t * is the largest fraction of contract every GBR flow can hold at once. t* = 1 means the set is feasible, the floor binds nothing, and stage A is free — which is why it is on by default. α trades the guarantee against throughput.

## Slide 5
THE DESIGN · EVERY SLOT
Tier-2: hit that target, slot by slot
Every flow carries a virtual queue — an accumulator in bits, not a buffer of data:
Q_i += r_i·Δ ; Q_i ← min(Q_i, ceil_i)
grow by the Tier-1 target, then clamp
serve ; Q_i ← max(0, Q_i − delivered_i)
ceil_i = max(0, min(r_i·W, A_i^W) − D_i^W)
the debt the flow legitimately accrued over the window W
Ranking, and then the transport block:
Q̃_i = Q_i + w_d·(HoL_i/PDB_i)^κ · max_j Q_j
deadline urgency, scaled by the system-wide max queue
M_u = ( Σ_{i∈u} Q̃_i ) · SE_u
rank UEs — opportunistic and rate-tracking at once
fill the TB by TS 38.321 LCP: priority, then Q̃_i
Q_i is a non-saturating integrator, so it can reach an arbitrary, unequal target vector — precisely what a multiplicative urgency metric cannot do at any weight.
Clamping to a windowed arrival count, not instantaneous backlog: a bursty video flow empties between frames, and clamping there erases its legitimate debt.
Configured grants carry the periodic flows — standing allocations in priority tiers, self-gating where they would starve the dynamic pool.

## Slide 6
EVALUATION
The simulator: what it models, and what it does not
Modelled
• The slot-by-slot PRB grid, with the TDD special slot
• The PDCCH/CCE budget, with DCI aggregation levels
• The uplink BSR round-trip — delay plus loss
• CQI delay and loss; BLER from MCS/SNR mismatch
• Per-UE AR(1) SNR through an MCS staircase
• Per-flow buffers, HoL timestamps, PDB expiry
Not modelled
• LDPC and I/Q; HARQ as a state machine — a fixed delay and a BLER discount instead
• Per-packet RLC segmentation, MU-MIMO
• Mobility, UE churn, inter-cell interference
So the results are comparative, not absolute — and what we omit would widen the configured-grant margin, not narrow it.
Three workloads, each sized so a different bottleneck binds:
Scenario | Carrier / TDD | Workload | What binds
factory_robots | 40 MHz, μ=2, DSUUU | 10 robots, 24 flows, 14–24 dB | Uplink data channel
sensor_dense | 30 MHz, μ=1, DSUUU | 30 periodic sensors, 15 ms PDB | PDCCH / CCE budget
latency_bound | 40 MHz, μ=1, DDDSU | 8 × 5 Mbps + 80 Mbps bulk | Deadlines under saturation

## Slide 7
SENSOR_DENSE · THE CONTROL CHANNEL BINDS
Result 1: a capability PF does not have
30 dense periodic uplink sensors with a 15 ms deadline. The DCI/CCE budget runs out before the data channel does.
Scheduler | Total | On time | Min delivery | Worst p99
Round Robin | 6.9 M | 0/30 | 71% | 15.0 ms
Proportional Fair | 9.2 M | 2/30 | 85% | 15.0 ms
Two-tier | 9.6 M | 30/30 | 100% | 5.0 ms
Each periodic flow gets a standing allocation that costs zero PDCCH per slot and needs no BSR round trip. PF is throttled by both budgets at once and has no mechanism to bypass either — so no amount of PF tuning closes this.
Larrañaga et al. (JNCA 2023) report the same dominance of configured grants for time-critical industrial traffic from ns-3 / 5G-LENA — an independent simulator sharing no code with ours.

## Slide 8
LATENCY_BOUND · DEADLINES UNDER SATURATION
Result 2: deadline-blindness is silent
Eight interactive 5 Mbps streams with a 12 ms deadline, sharing a saturated downlink with 80 Mbps of bulk.
Scheduler | On time | Mean delivery | Worst p99 | Bulk carried
Round Robin | 3/8 | 84% | 12.0 ms | 22.8 M
Proportional Fair | 5/8 | 86% | 12.0 ms | 24.6 M
Two-tier | 8/8 | 100% | 4.5 ms | 13.2 M
PF's mean delivery on the control flows is 86% — which reads healthy on a dashboard. The missing 14% are aged-out packets: the late motion commands, the safety-relevant ones. Mean delivery is not a safety metric.
The design pays for this explicitly and visibly — bulk throughput drops 24.6 → 13.2 Mbps to clear every deadline. That is the trade the QoS profile asked for.

## Slide 9
FACTORY_ROBOTS · THE UPLINK DATA CHANNEL BINDS
Result 3: rate contracts, swept across offered load
Ten robots, uplink-heavy. Capacity is fixed by spectrum, so the swept axis is offered load.
Chart: Worst-served GBR flow (% of contract)
| 1.00x | 0.67x | 0.50x | 0.33x
Proportional Fair | 1 | 21 | 52 | 83
Two-tier | 44 | 67 | 81 | 83
Contracts met (≥95% of the rate floor)
Load | PF | Two-tier
1.00x (as shipped) | 1/10 | 0/10
0.67x | 6/10 | 1/10
0.50x | 8/10 | 10/10
0.33x | 10/10 | 10/10
At 0.50× we honour 10/10 contracts to PF's 8/10. Deeper in overload the two disagree about the metric, not the outcome: at 0.67× every robot holds ≥67% of its rate where PF's worst gets 21%.
A threshold count rewards concentrating the shortfall; the max-min floor spreads it, and α picks between them. This deep into overload the operator's real lever is admission control.

## Slide 10
SUMMARY
What the design adds — and what it costs
Added over the PF baseline
• A rate contract that is stated and honoured — 10/10 against 8/10 at moderate load; worst-served 44% against 1% in overload.
• A deadline that is tracked, not hoped for — 8/8 against 5/8, p99 4.5 against 12.0 ms.
• A control-channel path for dense periodic traffic — 30/30 against 2/30 where the CCE budget binds.
• A single fairness dial that self-disables when the GBR set is feasible, plus soft per-slice floors.
Paid for with
• About 4% of aggregate throughput at the max-min floor in deep overload — the price of holding the worst-served flow above zero.
• One convex solve per second — CVXPY/Clarabel here, GLPK simplex with successive convex approximation in the OAI port.
• Per-5QI priority and prioritised-bit-rate configuration that has to actually be set.
It is also markedly less sensitive to control-plane fidelity. Sweeping the uplink BSR round-trip from 0 to 16 slots, PF's contract count breaks 8/10 → 5/10 and its worst-served flow falls 66% → 30%; the two-tier design moves 10/10 → 8/10 and 80% → 77%, losing 1% of throughput against PF's 10%. Configured-grant flows are invariant to BSR delay by construction.

## Slide 11
STATUS
Where this stands, and what remains
Built and tested
• Scheduler library: Tier-1, Tier-2, configured grants, per-UE grants with a TS 38.321 multiplexer, per-slice floors
• A symbol-accurate NR simulator with PDCCH, BSR and CQI models
• Three scenario studies, 70 regression tests, one script per result table
In progress
• OAI integration in a separate repo — Tier-1 as GLPK simplex with successive convex approximation, Tier-2 inside the NR MAC
• Porting the max-min stage and the per-5QI priority mapping onto that branch
To test on hardware
• End-to-end runs on OAI with COTS UEs
• Tier-1 solve time inside a real 1 s budget
• What the simulator omits: HARQ PRB cost, uplink grant timing, mobility, UE churn
• Multi-cell and inter-cell interference
The design is settled and the simulation case is made: against the PF scheduler OAI ships, it adds rate contracts, deadline tracking and a control-channel path, at a cost we can state and bound. The open work is landing it on real hardware — everything above is comparative, in a simulator, and silicon is the next step.